## Slide 1
Reactance and Impedance, LC oscillation (qualitative treatment only),
CLASS-XII
SUBJECT : PHYSICS
CHAPTER NUMBER: 07
CHAPTER NAME : ALTERNATING CURRENT

## Slide 2
LEARNING OUTCOME
After this lesson, students will be able:
Explain from where electricity comes and how we use it.
Define electrical energy in terms of charge, voltage, current and resistance.
Identify the types of engineering careers that work primarily with electrical energy.

## Slide 3
AC Circuit with a Pure Resistor:
R
E = E0 sin ωt
E = E0 sin ωt
I = E / R
= (E0 / R) sin ωt
I = I0 sin ωt
(where I0 = E0 / R and R = E0 / I0)
Emf and current are in same phase.
T/4 T/2 3T/4 T 5T/4 3T/2 7T/4 2T
t
0
π
2π
3π
4π
π/2
3π/2
5π/2
7π/2
θ = ωt
E ,I
E0
I0
E = E0 sin ωt
I = I0 sin ωt
E0
I0
ωt
y
x
0

## Slide 4
x
0
AC Circuit with a Pure Inductor:
L
E = E0 sin ωt
E = E0 sin ωt
T/4 T/2 3T/4 T 5T/4 3T/2 7T/4 2T
t
π
2π
3π
4π
π/2
3π/2
5π/2
7π/2
θ = ωt
E ,I
E0
I0
E = E0 sin ωt
I = I0 sin (ωt - π / 2)
E0
ωt
Induced emf in the inductor is - L (dI / dt)
In order to maintain the flow of current, the applied emf must be equal and opposite to the induced emf.
E = L (dI / dt)
E0 sin ωt = L (dI / dt)
dI = (E0 / L) sin ωt dt
I = ∫ (E0 / L) sin ωt dt
I = (E0 / ωL) ( - cos ωt )
I = I0 sin (ωt - π / 2)
(where I0 = E0 / ωL and XL = ωL = E0 / I0) XL is Inductive Reactance. Its SI unit is ohm.
I0
y
Current lags behind emf by π/2 rad.
0
π/2

## Slide 5
y
AC Circuit with a Capacitor:
E = E0 sin ωt
E = E0 sin ωt
T/4 T/2 3T/4 T 5T/4 3T/2 7T/4 2T
t
0
π
2π
3π
4π
π/2
3π/2
5π/2
7π/2
θ = ωt
E ,I
E0
I0
E = E0 sin ωt
I = I0 sin (ωt + π / 2)
E0
ωt
q = CE = CE0 sin ωt
I = dq / dt
= (d / dt) [CE0 sin ωt]
I = [E0 / (1 / ωC)] ( cos ωt )
I = I0 sin (ωt + π / 2)
(where I0 = E0 / (1 / ωC) and
XC = 1 / ωC = E0 / I0) XC is Capacitive Reactance. Its SI unit is ohm.
I0
π/2
x
0
Current leads the emf by π/2 radians.
C

## Slide 6
Variation of XL with Frequency:
I0 = E0 / ωL and XL = ωL
XL is Inductive Reactance and ω = 2π f
XL = 2π f L i.e. XL α f
XL
f
0
Variation of XC with Frequency:
I0 = E0 / (1/ωC) and XC = 1 / ωC
XC is Inductive Reactance and ω = 2π f
XC = 1 / 2π f C i.e. XC α 1 / f
XC
f
0
TIPS:
Inductance (L) can not decrease Direct Current. It can only decrease Alternating Current.
Capacitance (C) allows AC to flow through it but blocks DC.

## Slide 7
L C Oscillations:
C
L
C
L
C
L
+ + + + +
- - - - -
C
L
+ + + + +
- - - - -
C
L
+ + +
- - -
C
L
+ + +
- - -
C
L
+ + +
- - -
C
L
+ + +
- - -
C
L
+ + + + +
- - - - -
At t = 0, UE=Max. & UB=0
At t = T/8, UE = UB
At t =3T/8, UE = UB
At t = 4T/8, UE=Max. & UB=0
At t = 2T/8, UE=0 & UB=Max.
At t =T, UE=Max. & UB=0
At t =5T/8, UE = UB
At t = 6T/8, UE=0 & UB=Max.
At t =7T/8, UE = UB

## Slide 8
q
q0
q
q0
Undamped Oscillations
Damped Oscillations
If q be the charge on the capacitor at any time t and dI / dt the rate of change of current, then
or L (d2q / dt2) + q / C = 0
or d2q / dt2 + q / (LC) = 0
Putting 1 / LC = ω2
d2q / dt2 + ω2 q = 0
The final equation represents Simple Harmonic Electrical Oscillation with ω as angular frequency.
So, ω = 1 / √LC
or
L dI / dt + q / C = 0
t
0
t
0
2π √LC
1
f =

## Slide 9
HOME ASSIGNMENT
Two bulbs are rated (If they are connected (i) in series and (ii) in parallel across a supply V, find the power dissipated in the two combinations in terms of and .
Two electric bulbs P and Q have their resistances in the ratio of 1:2. They are connected in series across a battery. Find the ratio of the power dissipation in these bulbs.
3. A 25 W and a 100W bulb are joined in (i) series (ii) parallel and connected to the main. Which bulb glows brighter?

## Slide 10
THANKING YOU
ODM EDUCATIONAL GROUP