## Slide 1
LCR series circuit, resonance,
CLASS-XII
SUBJECT : PHYSICS
CHAPTER NUMBER: 07
CHAPTER NAME : ALTERNATING CURRENT

## Slide 2
LEARNING OUTCOME
After this lesson, students will be able:
Explain from where electricity comes and how we use it.
Define electrical energy in terms of charge, voltage, current and resistance.
Identify the types of engineering careers that work primarily with electrical energy.

## Slide 3
AC Circuit with L, C, R in Series Combination:
E = E0 sin ωt
C
L
R
VL
VC
VR
In R, current and voltage are in phase.
In L, current lags behind voltage by π/2
In C, current leads the voltage by π/2
VR
VL
VC
I
π/2
π/2
- VC
VL
VR
I
π/2
VL - VC
VR
I
E
Φ
E = √ [VR2 + (VL – VC)2]
The applied emf appears as Voltage drops VR, VL and VC across R, L and C respectively.
E = √ [VR2 + (VL – VC)2]
I =
E
√ [R2 + (XL – XC)2]
Z = √ [R2 + (XL – XC)2]
Z = √ [R2 + (ω L – 1/ωC)2]
tan Φ =
XL – XC
R
tan Φ =
ω L – 1/ωC
R
or
0
VC

## Slide 4
or
tan Φ =
XL – XC
R
tan Φ =
ω L – 1/ωC
R
Special Cases:
Case I: When XL > XC i.e. ω L > 1/ωC,
tan Φ = +ve or Φ is +ve
The current lags behind the emf by phase angle Φ and the LCR circuit is inductance - dominated circuit.
Case II: When XL < XC i.e. ω L < 1/ωC,
tan Φ = -ve or Φ is -ve
The current leads the emf by phase angle Φ and the LCR circuit is capacitance - dominated circuit.
Case III: When XL = XC i.e. ω L = 1/ωC,
tan Φ = 0 or Φ is 0°
The current and the emf are in same phase. The impedance does not depend on the frequency of the applied emf. LCR circuit behaves like a purely resistive circuit.

## Slide 5
Resonance in AC Circuit with L, C, R:
When XL = XC i.e. ω L = 1/ωC, tan Φ = 0 or Φ is 0° and
Z = √ [R2 + (ω L – 1/ωC)2] becomes Zmin = R and I0max = E / R
i.e. The impedance offered by the circuit is minimum and the current is maximum. This condition is called resonant condition of LCR circuit and the frequency is called resonant frequency.
At resonant angular frequency ωr,
ωr L = 1/ωrC or ωr = 1 / √LC or fr = 1 / (2π √LC)
ωr
I0max
ω
0
R1
R2
R3
I0
I0max / √2
ωr - ∆ ω
ωr + ∆ ω
Band width = 2 ∆ ω
Quality factor (Q – factor) is defined as the ratio of resonant frequency to band width.
Q = ωr / 2 ∆ ω
or Q = ωr L / R
or Q = 1 / ωrCR
Q = VL / VR
or Q = VC / VR
Resonant Curve & Q - Factor:
It can also be defined as the ratio of potential drop across either the inductance or the capacitance to the potential drop across the resistance.
R1 < R2 < R3

## Slide 6
Power in AC Circuit with L, C, R:
Instantaneous Power = E I
= E0 I0 sin ωt sin (ωt + Φ)
= E0 I0 [sin2 ωt cosΦ + sin ωt cosωt cosΦ]
E = E0 sin ωt
I = I0 sin (ωt + Φ) (where Φ is the phase angle between emf and current)
If the instantaneous power is assumed to be constant for an infinitesimally small time dt, then the work done is
dW = E0 I0 [sin2 ωt cosΦ + sin ωt cosωt cosΦ]
Work done over a complete cycle is
W = ∫ E0 I0 [sin2 ωt cosΦ + sin ωt cosωt cosΦ] dt
0
T
W = E0I0 cos Φ x T / 2
Average Power over a cycle is Pav = W / T
Pav = (E0I0/ 2) cos Φ
Pav = (E0/√2) (I0/ √2) cos Φ
(where cos Φ = R / Z
= R /√ [R2 + (ω L – 1/ωC)2] is called Power Factor)
Pav = Ev Iv cos Φ

## Slide 7
Ev
Power in AC Circuit with R:
In R, current and emf are in phase.
Φ = 0°
Pav = Ev Iv cos Φ = Ev Iv cos 0° = Ev Iv
Power in AC Circuit with L:
In L, current lags behind emf by π/2.
Φ = - π/2
Pav = Ev Iv cos (-π/2) = Ev Iv (0) = 0
Power in AC Circuit with C:
In C, current leads emf by π/2.
Φ = + π/2
Pav = Ev Iv cos (π/2) = Ev Iv (0) = 0
Note:
Power (Energy) is not dissipated in Inductor and Capacitor and hence they find a lot of practical applications and in devices using alternating current.
Pav = Ev Iv cos Φ
Wattless Current or Idle Current:
Iv
Iv cos Φ
Iv sin Φ
Φ
90°
The component Iv cos Φ generates power with Ev.
However, the component Iv sin Φ does not contribute to power along Ev and hence power generated is zero. This component of current is called wattless or idle current.
P = Ev Iv sin Φ cos 90° = 0

## Slide 8
HOME ASSIGNMENT
Two bulbs are rated (If they are connected (i) in series and (ii) in parallel across a supply V, find the power dissipated in the two combinations in terms of and .
Two electric bulbs P and Q have their resistances in the ratio of 1:2. They are connected in series across a battery. Find the ratio of the power dissipation in these bulbs.
3. A 25 W and a 100W bulb are joined in (i) series (ii) parallel and connected to the main. Which bulb glows brighter?

## Slide 9
THANKING YOU
ODM EDUCATIONAL GROUP