## Slide 1
A.C. generator
CLASS-XII
SUBJECT : PHYSICS
CHAPTER NUMBER: 07
CHAPTER NAME : ALTERNATING CURRENT

## Slide 2
LEARNING OUTCOME
After this lesson, students will be able:
Explain from where electricity comes and how we use it.
Define electrical energy in terms of charge, voltage, current and resistance.
Identify the types of engineering careers that work primarily with electrical energy.

## Slide 3
S
A.C. Generator:
A.C. Generator or A.C. Dynamo or Alternator is a device which converts mechanical energy into alternating current (electrical energy).
N
P
Q
R
S
R1
R2
B1
B2
Load
S
R
R1
R2
B1
B2
Load
N
Q
P
S

## Slide 4
A.C. Generator is based on the principle of Electromagnetic Induction.
Principle:
Field Magnet with poles N and S
Armature (Coil) PQRS
Slip Rings (R1 and R2)
Brushes (B1 and B2)
Load
Construction:
Working:
Let the armature be rotated in such a way that the arm PQ goes down and RS comes up from the plane of the diagram. Induced emf and hence current is set up in the coil. By Fleming’s Right Hand Rule, the direction of the current is PQRSR2B2B1R1P.
After half the rotation of the coil, the arm PQ comes up and RS goes down into the plane of the diagram. By Fleming’s Right Hand Rule, the direction of the current is PR1B1B2R2SRQP.
If one way of current is taken +ve, then the reverse current is taken –ve.
Therefore the current is said to be alternating and the corresponding wave is sinusoidal.

## Slide 5
Theory:
P
Q
R
S
B
θ
ω
n
Φ = N B A cos θ
At time t, with angular velocity ω,
θ = ωt (at t = 0, loop is assumed to be perpendicular to the magnetic field and θ = 0°)
Φ = N B A cos ωt
Differentiating w.r.t. t,
dΦ / dt = - NBAω sin ωt
E = - dΦ / dt
E = NBAω sin ωt
E = E0 sin ωt (where E0 = NBAω)
0
π
2π
3π
4π
T/4 T/2 3T/4 T 5T/4 3T/2 7T/4 2T
t
π/2
3π/2
5π/2
7π/2
θ = ωt
E0
End of Alternating Currents

## Slide 6
HOME ASSIGNMENT
Two bulbs are rated (If they are connected (i) in series and (ii) in parallel across a supply V, find the power dissipated in the two combinations in terms of and .
Two electric bulbs P and Q have their resistances in the ratio of 1:2. They are connected in series across a battery. Find the ratio of the power dissipation in these bulbs.
3. A 25 W and a 100W bulb are joined in (i) series (ii) parallel and connected to the main. Which bulb glows brighter?

## Slide 7
THANKING YOU
ODM EDUCATIONAL GROUP